Table I:  Software Product Matrix

| Product | Bandscope width [max] | Linux | Windows | Receive | Transmit | Xpol Receive | Hardware | Noise Reduction | Open Source |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Linrad | No Limit [Hardware-determined] | Yes | Yes | Yes | Can control external transceiver frequency | Yes | WSE SDR-14 SDR-IQ Any I/Q | Yes | Yes |
| Winrad | 192 kHz | No | Yes | Yes | External I/O dll available | No | WSE SDR-14 SDR-IQ Any I/Q | Yes | No |
| PowerSDR | 192 kHz | No | Yes | Yes | Yes | No | SDR-1000 Flex-5000 Softrock Any I/Q [rx] | Yes | Yes |
| Rocky | 96 kHz [some cards won't work properly at 96 kHz] | No | Yes | Yes | User implemented | No | Softrock40 Any I/Q | No | No |
| DttSP | Depends on Software and Hardware | Yes | Yes | Yes | Yes | No | SDR-1000 Flex-5000 Any I/Q [rx] | Yes | Yes |
| SpectraVue | 30 MHz w/no demod 150 kHz w/demod | No | Yes | Yes | No | No | SDR-14 SDR-IQ Any I/Q | No | No |

Table II :  Software Product Matrix Part 2

| Product | Effectiveness | Versatiliity | Learning Curve | Special Hardware To Calibrate | Multiple Instances * |
| --- | --- | --- | --- | --- | --- |
| Linrad | Smart/Dumb Noiseblanker combination is unsurpassed. Filters are very effective. | Extremely adaptable; several pages of parameters which can be adjusted. | Steep, due to versatility. To begin, just accept the default parameters and go. Documentation is voluminous but sometimes opaque. | Using Smart Blanker requires calibration with a pulser producing 5 volt pulses at prf 100-200 Hz, duration 5 nsec. I use TekPG50B 50 MHz pulser set to prf 200 Hz, no delay, 0.1 ms duration, 5 ns transition time, and 5 volts | Yes. |
| Winrad | Good. | Good. | Fairly simple to learn. | No | Yes. |
| PowerSDR | Very Good | Very Good. | Easy learning curve, well documented | No. | Should be possible with new versions. |
| Rocky | Signal enhancement is rudimentary [bandpass filters]. | Not designed for weak signal work. | Simple. | No. | No. |
| DttSP | Signal enhancement is under construction. | Good. | Steep, not well documented. | No. | Yes. |
| SpectraVue | Signal enhancement is rudimentary [bandpass filters]. | Not designed for weak signal work. | Simple. | No | No. |

* http://groups.yahoo.com/group/softrock40/message/5593

Table III:  Hardware Product Matrix

| Product | Bandscope width [max] | Software | Receive | Transmit | Xpol Receive | Frequency Range | IP3 [dBm] | Price | Image Rejection |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| WSE SM5BSZ | 96 kHz | Linrad / Any | Yes | No | Yes | Ham Bands 160-20M, 2M | 2M: > +27 HF: +32 | $2200 [variable due to SEK/$] | Excellent |
| Flex-5000 | 192 kHz | PowerSDR | Yes | Yes | No | 1.8 - 60 MHz 12 kHz-60 MHz receive | +33 | $2499 | Excellent |
| SDR-1000 | 192 kHz | PowerSDR | Yes | Yes | No | 1.8 - 60 MHz 12 kHz-60 MHz receive | +26 | Not Available | Excellent |
| SDR-1000 clone KDG-SR100 | 192 kHz | PowerSDR | Yes | Yes | No | 1.8-60 MHz 12 kHz-60 MHz receive | +9 | $860 | Excellent |
| SDR-14 | 190 kHz 30 MHz w/o demod | SpectraVue Linrad Winrad/Any | Yes | No | No | 50 kHz-30 MHz [50 kHz-230 MHz direct] | NA | $1100 | Excellent |
| SDR-IQ | 190 kHz | SpectraVue Linrad Winrad/Any | Yes | No | No | 500 Hz-30 MHz | +15 [with dither] | $400 OEM board $500 boxed* | Excellent |
| Softrock | Software-dependent | Rocky Linrad/Any | Yes | Some models | Possible with two | 160-30M 10M sold out. | varies by model 30M: +18 | $36 for 160M or 20/30M xcvr | Poor to Fair |
| Time Machine | Software-dependent | Linrad Winrad/Any | Yes | No | No | 160-10M with appropriate filters |  | $135 kit $170 assembled | Fair |
| HPSDR/ TAPR Atlas/ Ozy/Janus | 192 kHz | PowerSDR | Yes | Yes | No | Used with SDR-1000 [see text] | N/A | $356 $325 disc. | Excellent |